## Slide 1: Science DMZ for ESGF Supernodes
Eli Dart, Network Engineer
ESnet Science Engagement
Lawrence Berkeley National Laboratory
2015 ESGF Conference
Monterey, CA
December 10, 2015

## Slide 2: Outline
Science DMZ intro – motivation and summary
Reconsidering architecture
Possible future ESGF deployment design

## Slide 3: Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
© 2015, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 4: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
For ESGF this means several things
  Distributed ESGF data archive enabled by networks
  Portal services accessed over networks
  Leverage networks to keep up with data scale
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
© 2015, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 5: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
  Packet loss in conjunction with latency is a performance killer
© 2015, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 6: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2015, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 7: Science DMZ Design Pattern (Abstract)
© 2015, Energy Sciences Network
Notes: This is an abstract cartoon – nobody’s network looks exactly like this
The diagram has no management LAN, no terminal servers, etc.
However, this is the minimum network diagram that shows the essential Science DMZ components:
Science DMZ enclave
DTN
perfSONAR (in the WAN, at the border, in the Science DMZ)
Security policy controls

## Slide 8: Science DMZ for Major ESGF Nodes
Many (most?) ESGF deployments combine many services on a few systems
  Components could be separated, but often they are not
  Significant complexity
  Performance limitations
Improve performance by separating data download piece
  Place data server in Science DMZ
  Leave the rest of the portal where it is
Requires a change in deployment architecture

## Slide 9: Example of Architectural Change – CDN
Let’s look at what Content Delivery Networks did for web applications
CDNs are a well-deployed design pattern
  Akamai and friends
  Entire industry in CDNs
  Assumed part of today’s Internet architecture
What does a CDN do?
  Store static content in a separate location from dynamic content
    Complexity isn’t in the static content – it’s in the application dynamics
    Web applications are complex, full-featured, and slow
      Databases, user awareness, etc.
      Lots of integrated pieces
    Data service for static content is simple by comparison
  Separation of application and data service allows each to be optimized

## Slide 10: Classical Web Server Model
Web browser fetches pages from web server
  All content stored on the web server
  Web applications run on the web server
    Web server may call out to local database
    Fundamentally all processing is local to the web server
  Web server sends data to client browser over the network
Perceived client performance changes with network conditions
  Several problems in the general case
  Latency increases time to page render
  Packet loss + latency causes problems for large static objects

## Slide 11: Solution: Place Large Static Objects Near Client
CDN provides static content “close” to client
  Latency goes down
    Time to page render goes down
    Static content performance goes up
  Load on web server goes down (no need to serve static content)
  Web server still manages complex behavior
    Local reasoning / fast changes for application owner
Significant win for web application performance

## Slide 12: Client Simply Sees Increased Performance
Client doesn’t see the CDN as a separate thing
  Web content is all still viewed in a browser
    Browser fetches what the page tells it to fetch
    Different content comes from different places
    User doesn’t know/care
CDNs provide an architectural solution to a performance problem
  Not brute-force
  Work smarter, not harder

## Slide 13: Architectural Examination of Data Portals
Common data portal functions (most portals have these)
  Search/query/discovery
  Data download method for data access
  GUI for browsing by humans
  API for machine access – ideally incorporates search/query + download
Performance pain is primarily in the data download piece
  Rapid increase in data scale eclipsed legacy software stack capabilities
  Portal servers often stuck in enterprise network
Can we “disassemble” the portal and put the pieces back together better?
  Use Science DMZ as a platform for the data piece
  Avoid placing complex software in the Science DMZ

## Slide 14: ESGF Node With Separate DTNs

## Slide 15: Defense In Depth – Security Controls

## Slide 16: Potential ESGF Deployment Changes
Separate DTNs in a Science DMZ offer significant performance benefits
One possible scenario – DTNs run GridFTP/Globus only
  HTTP/wget access remains as it is
  GridFTP URLs point to DTNs
I have heard from several folks that the software supports this
  Separation of components
  Ability to run different services on different hosts (in different networks)
Deployment model is all that needs to change

## Slide 17: Thanks!
Eli Dart
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
http://fasterdata.es.net/
http://my.es.net/
http://www.es.net/